## Slide 1
High Bandwidth Memory (HBM4/HBM4E)
Presented by: Jai Akash T
Register Number: 243115106037
Class Section: ECE-3A
A simple guide to the 3D-stacked vertical silicon chip structures, microscopic vertical copper wire connects, and high-speed lanes powering next-gen AI supercomputers.

## Slide 2
Memory Bottleneck in Modern AI Computing
THE LAYMAN WAREHOUSE ANALOGY
DDR Memory is like a warehouse built far away from the factory (GPU).
Trucks (signals) take a long time to travel back and forth on narrow highways.
HBM4 stacks 16 warehouses directly on top of the factory and links them using fast elevators.
TECHNICAL CHALLENGES WITH DDR
Processor Speeds have scaled up by 1000x over recent years.
Memory Bandwidth has only grown by 10x, leaving high-performance engines starving for data.
Flat Motherboard designs have hit a physical routing limit, preventing wider data highways.

## Slide 3
Evolution of High Bandwidth Memory
HBM1 (2013): 1st gen stack with 1024-bit width. 1 GB capacity, 128 GB/s bandwidth.
HBM2 (2016): Capacity expanded to 8 GB. Pins rate scaled to 2.0 Gbps (256 GB/s bandwidth).
HBM3 (2022): 24 GB capacity. Pin rate scaled up to 6.4 Gbps, yielding 819 GB/s bandwidth.
HBM3E (2024): 36 GB capacity, transferring data speeds up to 9.6 Gbps (1.2 TB/s bandwidth).
HBM4 (2025/2026): Doubled bus width (2048-bit). Custom logic base dies on advanced foundry nodes.

## Slide 4
HBM4 Architectural Breakdown
Silicon Interposer: The horizontal silicon highway that connects the GPU side-by-side with the HBM Memory stack.
Custom Logic Base Die: The buffer control die at the bottom. Built on advanced foundry nodes (TSMC N5) to schedule data.
DRAM Stack (12/16-High): Paper-thin memory layers stacked vertically on top of the logic base to packing storage capacity.
Microbumps & TSVs: Microscopic vertical copper wires drilled straight through silicon layers to connect stacked DRAM.

## Slide 5
3D Stacking & Processor Access Simulation
HBM4 stacks memory layers vertically to bypass physical spacing limits, integrating 4 core operations:
Instruction Fetch (IF): High-speed green data flows routing instruction codes from HBM stack to CPU cores.
Data Read (RD): Standard blue signals transferring operands and parameters from HBM columns to GPU cores.
Data Write (WR): Pink data signals routing processed calculations back from GPU cores into DRAM cell rows.
Memory Refresh (RF): Amber sequencing sweeps that periodically recharge capacitive cells inside DRAM dies.

## Slide 6
Performance Metrics & Specifications
BANDWIDTH PERFORMANCE
DDR5: 38.4 GB/s (Baseline flat bus)
GDDR7: 192 GB/s (Dedicated graphics standard)
HBM3E: 1228 GB/s (Legacy stacked standard)
HBM4: 2048 GB/s (Widescreen 2048-bit bus standard)
HBM4E: 2457+ GB/s (Enhanced performance peak)
Feature Metric | HBM4 Standard | HBM4E (Enhanced)
Max Capacity | Up to 48 GB | Up to 64 GB
Bus Width | 2048-bit / 32 Ch | 2048-bit / 32 Ch
Data Pin Speed | 8.0 Gbps | 9.6+ Gbps
Peak Bandwidth | 2.0 TB/s | 2.45+ TB/s
Logic Node | TSMC Custom N5 | TSMC Custom N5
Stacking Height | 12 / 16 Layers | 12 / 16 Layers

## Slide 7
Manufacturing & Thermal Management
3D MANUFACTURING WORKFLOW
01. TSV Drilling: Deep RIE lasers drill microscopic channels straight through wafers, filling them with copper to construct vertical conduits.
02. Wafer Thinning: Silicon substrates are ground down to paper-thin ~30μm dimensions to enable multi-layered stacking heights.
03. Hybrid Bonding: Direct atomic Copper-to-Copper fusion merges DRAM layers together, dropping pad pitches below 10μm.
THERMAL HEAT DISSIPATION MAP
Thermal Penalty: Stacking 16 hot memory layers traps high-power heat in the core logic.
TIM Materials: Advanced interface materials with high thermal conductivity conduct heat up to top lids.
Dummy Vias: Unconnected dummy TSVs are placed inside memory layers to act as passive heat pipeline guides.
Top cap: 45°C | Stack core: 78°C | Logic die: 60°C

## Slide 8
THANK YOU